## Slide 1: Chapter 40
Respiratory Support and Therapies

## Slide 2: Respiratory Support and Therapies
Some persons need:
  Artificial airways
  Suctioning
  Mechanical ventilation
  Chest tubes
Often, very ill persons need:
  Respiratory rehabilitation
  To recover from problems affecting the airways and lungs
  Complex procedures and equipment
Notes: The nurse may ask you to assist with the person’s care.
See Body Structure and Function Review: The Respiratory System (Chapter 39) in the Textbook.

## Slide 3: Artificial Airways
Artificial airways keep the airway patent (open and unblocked).
  They are needed:
    When disease, injury, secretions, or aspiration obstructs the airway
    For mechanical ventilation
    By some persons who are semi-conscious or unconscious
    When the person is recovering from anesthesia

## Slide 4: Artificial Airways (Cont.)
Intubation means inserting an artificial airway.
These airways are common.
  Oropharyngeal airway—inserted through the mouth and into the pharynx
  Endotracheal (ET) tube—inserted through the mouth or nose and into the trachea
    A cuff is inflated to keep the airway in place.
  Tracheostomy tube—inserted through a surgically created opening into the trachea
    Cuffed tubes are common.
Notes: Artificial airways are usually plastic and disposable. They come in various sizes.
A nurse or a respiratory therapist (RT) inserts an oropharyngeal airway.
A doctor inserts an endotracheal (ET) tube using a lighted scope. Some RNs and respiratory therapists are trained to insert ET tubes.
Doctors perform tracheostomies. The cuff is inflated to keep the tube in place.

## Slide 5: Artificial Airways (Cont.)
Care measures
  Vital signs and pulse oximetry are measured often.
  Observe for hypoxia and other signs and symptoms.
  If an airway comes out or is dislodged, tell the nurse at once.
  Frequent oral hygiene is needed.
    Follow the care plan.
  Comfort and reassure the person.
  Follow the care plan for communication methods.
  Always keep the signal light within reach.
Notes: Gagging and choking feelings are common. Remind the person that the airway helps breathing.
Use touch to show you care.
Review the Focus on Communication: Artificial Airways Box on p. 659 in the Textbook.
Persons with ET tubes cannot speak. There are several ways to communicate:
  Paper and pencils
  Magic Slates and communication boards
  Hand signals, nodding the head, and hand squeezes are common for simple “yes” and “no” questions.

## Slide 6: Artificial Airways (Cont.)
A tracheostomy is a surgically created opening into the trachea.
  Tracheostomies are temporary or permanent.
  A tracheostomy tube has three parts.
    The obturator is used to guide the insertion of the outer cannula (tube).
    The inner cannula is inserted and locked in place.
    The outer cannula is not removed.
  The tube must not come out (extubation).
  A loose tube can damage the trachea.
  The tube must remain patent.
    If able, the person coughs up secretions. Otherwise suctioning is needed.
Notes: Tracheostomies are permanent when airway structures are surgically removed. Cancer, severe airway trauma, or brain damage may require a permanent tracheostomy.
The obturator is placed within easy reach in case the tracheostomy tube falls out and needs re-insertion.
The inner cannula fits inside the outer cannula. It is removed for cleaning and mucus removal. Some inner cannulas are disposable. Some tracheostomy tubes do not have inner cannulas.
The outer cannula is secured in place with ties around the neck or a Velcro collar.
The cuffed tracheostomy tube provides a seal between the cannula and the trachea. This prevents air from leaking around the tube. It also prevents aspiration.

## Slide 7: Artificial Airways (Cont.)
  Call for the nurse if:
    You note signs and symptoms of hypoxia or respiratory distress.
    The outer cannula comes out.
  Nothing must enter the stoma.
    Otherwise, the person can aspirate.
  Tracheostomy care involves:
    Cleaning the inner cannula to remove mucus and keep the airway patent
    Cleaning the stoma to prevent infection and skin breakdown
    Applying clean ties or a Velcro collar to prevent infection
Notes: The safety measures on p. 660 in the Textbook are needed.
The nurse may ask you to assist with tracheostomy care (trach care). The care is done daily or every 8 to 12 hours and as needed for excess secretions, soiled ties or collar, or soiled or moist dressings.
Disposable inner cannulas are discarded after one use. A new one is inserted. Re-usable inner cannulas are cleaned with a small bottle brush or a pipe cleaner. The nurse tells you what cleaning agent is needed.
Clean ties are applied before removing the dirty ones. Hold the outer cannula in place when the nurse changes the ties or collar.
Review the Focus on Children and Older Persons: Assisting with Tracheostomy Care Box on p. 660 in the Textbook.

## Slide 8: Suctioning the Airway
Secretions can collect in the airway.
  Retained secretions
    Obstruct air flow into and out of the airway
    Provide an environment for microbes
    Interfere with oxygen (O2) and carbon dioxide (CO2) exchange
Suctioning is needed for persons who cannot cough or whose cough is too weak to remove secretions.
  Suction is the process of withdrawing or sucking up fluid (secretions).
Notes: A suction source is needed—wall outlet or suction machine. A tube connects to a suction source at one end and to a suction catheter at the other end. The catheter is inserted into the airway. Secretions are withdrawn through the catheter.

## Slide 9: Suctioning the Airway (Cont.)
These routes are used to suction the airway.
  Oropharyngeal
    The mouth and pharynx are suctioned.
  Nasopharyngeal
    The nose and pharynx are suctioned.
  Lower airway
    The suction catheter is passed through an ET or tracheostomy tube.
    The person’s lungs are hyperventilated before suctioning an ET or a tracheostomy tube.
    An Ambu bag is attached to an oxygen source, and then the oxygen delivery device is removed. The bag is squeezed with both hands to give a breath.
Notes: The nose, mouth, and pharynx make up the upper airway. The trachea and bronchi make up the lower airway.
For oropharyngeal suction, a suction catheter is passed through the mouth and into the pharynx. The Yankauer suction catheter is often used for thick secretions.
For nasopharyngeal suction, the suction catheter is passed through the nose into the pharynx.
Oxygen is treated like a drug. You do not give drugs. You need to check if your state and agency allow you to use an Ambu bag attached to an oxygen source.
Review the Focus on Children and Older Persons: Suctioning Box on p. 662 in the Textbook.
Review the Promoting Safety and Comfort: Suctioning Box on p. 662 in the Textbook.
Box 40-1 on p. 661 in the Textbook lists the safety measures for assisting with suctioning.

## Slide 10: Mechanical Ventilation
Mechanical ventilation is using a machine to move air into and out of the lungs.
Mechanical ventilation is needed for a variety of health care problems, including:
  Weak muscle effort
  Obstructed airway
  Damaged lung tissue
  Nervous system diseases and injuries
  Drug overdose
Notes: Nervous system diseases and injuries can affect the respiratory center in the brain.
Nerve damage interferes with messages between the lungs and the brain.
Drug overdose depresses the brain.
With severe problems, the person cannot breathe or normal blood oxygen levels are not maintained.

## Slide 11: Mechanical Ventilation (Cont.)
An ET or tracheostomy tube is needed for mechanical ventilation.
  Alarms sound when something is wrong.
    One alarm means the person is disconnected from the ventilator.
    When any alarm sounds, first check to see if the person’s tube is attached to the ventilator.
    If not, attach it to the ventilator.
    Then tell the nurse at once about the alarm.
  Do not reset alarms.
  Persons needing mechanical ventilation are very ill.
    Some persons are confused and disoriented.
    The machine and fear of dying frighten many.
Notes: The nurse shows you how to reconnect the ET or tracheostomy tube.
The person can die if not attached to the ventilator.
Mechanical ventilation can be painful for those with chest injuries or chest surgery.
Tubes and hoses restrict movement. This causes more discomfort.
The nurse may ask you to assist with the person’s care. Review the contents of Box 40-2 on p. 663 in the Textbook.
Review the Focus on Long-Term Care and Home Care: Mechanical Ventilation Box on p. 663 in the Textbook.

## Slide 12: Chest Tubes
Air, blood, or fluid can collect in the pleural space (sac or cavity) when the chest is entered because of injury or surgery.
  Pneumothorax is air in the pleural space.
  Hemothorax is blood in the pleural space.
  Pleural effusion is the escape and collection of fluid in the pleural space.

## Slide 13: Chest Tubes (Cont.)
Pressure occurs when air, blood, or fluid collects in the pleural space.
  The pressure collapses the lung.
  Air cannot reach affected alveoli.
  O2 and CO2 are not exchanged.
    Respiratory distress and hypoxia result.
  Pressure on the heart affects the ability to pump blood.
The doctor inserts chest tubes to remove the air, blood, or fluid.
  Chest tubes attach to a drainage system.
    The system must be airtight.
    Water-seal drainage keeps the system airtight.
Notes: Hospital care is required.
The sterile procedure is done in surgery, in the emergency room, or at the bedside. A nurse assists.
Refer to Figures 40-8 and 40-9 on pp. 663-664 in the Textbook.
Review the care measures in Box 40-3 on p. 664 in the Textbook.